## Slide 1
COMPUTING / RESEARCH BRIEF
Quantum utility before fault tolerance
What a 127-qubit experiment demonstrated—and the limits of that claim.
Reading: Kim et al. · Nature 618, 500–505 (2023) · doi:10.1038/s41586-023-06096-3

## Slide 2
THE CLAIM
The result is meaningful—but narrower than ‘quantum advantage’
The paper treats utility as a step toward application advantage, not as proof of it.
Kim et al., Nature 618, 500–505 (2023), doi:10.1038/s41586-023-06096-3
02
What the experiment supports
What it does not establish
Scale
127-qubit superconducting processor; circuits reached 60 two-qubit-gate layers.
Recoverability
Mitigation recovered accurate expectation values in tested regimes beyond brute-force simulation.
Contribution
Noise characterization and control enabled the demonstrated circuit volumes.
Not broad advantage
The study explicitly does not claim a useful speed-up for a practical application.
Not fault tolerant
The processor remained noisy; error mitigation is not the same as error correction.
Not a universal threshold
Selected circuit families and observables do not prove all comparable tasks are classically intractable.

## Slide 3
THE EXPERIMENT
A 127-qubit chip ran 60 layers of two-qubit gates
A controlled many-body simulation made the noise question measurable.
Kim et al. (2023), abstract and main text. Circuit depth here means CNOT layers.
03
2D TRANSVERSE-FIELD ISING MODEL
Nearest-neighbour interactions mapped onto IBM Eagle’s heavy-hex connectivity.
1
2
3
4
5
6
7
8
ONE TROTTER STEP
01
Single-qubit X rotations set the transverse field.
02
Nearest-neighbour ZZ interactions are applied in parallel.
03
Three CNOT layers cover the heavy-hex neighbour pairs.
Benchmark: Trotterized 2D transverse-field Ising dynamics; the authors compare selected regimes to exact and approximate classical methods.

## Slide 4
METHOD
Noise compounds with depth; mitigation estimates the zero-noise limit
The intervention is a model-based correction to measured observables—not a noiseless processor.
Kim et al. (2023), main text, Figs. 1–2. ZNE = zero-noise extrapolation.
04
1 · Characterize
Learn local Pauli error rates for twirled CNOT layers.
→
2 · Scale noise
Execute circuits with controlled noise gains; measure each observable.
→
3 · Extrapolate
Fit measured values against noise gain to estimate the zero-noise value.
Trade-off: zero-noise extrapolation can reduce bias, but remains an estimate with residual bias and sampling cost.

## Slide 5
RESULTS
The demonstrated circuit scale is specific—and concrete
For the zero-field Clifford benchmark, ZNE improved agreement with the ideal magnetization at circuit depths up to 60 CNOT layers.
Kim et al. (2023), abstract and main text, Fig. 2. These metrics describe this experiment, not a general capability guarantee.
05
127
physical qubits on IBM Eagle (ibm_kyiv).
60
two-qubit CNOT layers reached in the reported experiments.
20
Trotter steps; the paper reports improved magnetization agreement after ZNE.
The strongest evidence is a validated workflow for selected observables at substantial circuit depth—not a practical application speed-up.

## Slide 6
INTERPRETATION
The correction works best when the benchmark is verifiable
Verification and computational hardness are not identical; the authors study both regimes.
Kim et al. (2023), main text, discussion of Clifford benchmark and 2D Ising circuits.
06
Exact-check regime
Harder-to-simulate regime
Clifford limit
When the transverse-field angle is a multiple of π/2, circuits become Clifford and admit efficient classical simulation. This gives a clear test of mitigation accuracy.
Strong entanglement
For strongly entangled circuits, the study compares with leading tensor-network approximations and reports regimes where they break down. That is not equivalent to ruling out every classical algorithm.
Good experimental reasoning uses tractable cases to validate the measurement pipeline, then separately examines harder cases.

## Slide 7
IMPLICATIONS
What this changes for quantum-computing research
A careful reading shifts the question from ‘how many qubits?’ to ‘which observable, at what cost, versus what classical baseline?’
Interpretation based on Kim et al. (2023), including its stated distinction between utility evidence and future application advantage.
07
Measure error, not just qubit count
Coherence and calibration improvements enabled this device’s depth; raw qubit count alone is a poor proxy for useful computation.
Treat mitigation as a method with assumptions
Noise models, stability, extrapolation choice and sampling overhead all affect whether corrected estimates are trustworthy.
Keep utility claims task-specific
Next steps require useful applications, comparative classical baselines, and costs that matter—not only circuits that exceed brute-force simulation.

## Slide 8
TAKEAWAY
The milestone is a capability demonstration—not the finish line
A bounded conclusion is stronger than an inflated headline.
Source: Kim et al. (2023), Nature 618, 500–505. https://doi.org/10.1038/s41586-023-06096-3
08
Noise-aware control made selected 127-qubit circuits useful for extracting accurate observables before fault tolerance.
The paper’s evidence supports quantum utility in a limited experimental sense. Demonstrating a practical quantum advantage remains a separate task: identify an application, beat the best classical approach, and account for resources.
PRIMARY SOURCE
Kim et al., “Evidence for the utility of quantum computing before fault tolerance,” Nature 618, 500–505 (2023). DOI: 10.1038/s41586-023-06096-3